Příloha č. 1

Technická specifikace předmětu veřejné zakázky

Core switche – 2 ks:
Specifikace:

•             24×100M/1G/2.5G/5G/10G Base-T Ethernet ports, 4×10GE SFP+

•             One extended slot

•             Double pluggable power supplies, AC/DC power supply

•             USB

•             Forwarding performance: 240 Mpps

•             Switching capacity: 2.56Tbps/23.04Tbps

•             Maximum power consumption - 108W(without card)

•             Memory (RAM) - 1 GB

•             Flash memory - 240 MB

•             Switching capacity - 2.56Tbps/23.04Tbps

•             Mean Time Between Failures (MTBF), years -  27.4

SECURITY

•             Defense against DoS, ARP, and ICMP attacks

•             Binding of the IP address, MAC address, port number, and VLAN ID of a user

•             Port isolation, port security, and sticky MAC

•             MAC-Forced Forwarding (MACFF)

•             Limit on the number of learned MAC addresses

•             IEEE 802.1X authentication, MAC address authentication, Portal authentication, and hybrid authentication

•             Authentication methods, including AAA, RADIUS, and HWTACACS

•             CPU defense

MANAGEMENT

•             iStack (using service ports as stack ports)

•             Virtual Cable Test (VCT)

•             Ethernet OAM (IEEE 802.3ah and 802.1ag)

•             SNMPv1/v2c/v3

•             RMON

•             Web-based network management system and relevant features

•             System logs and multi-level alarms

•             GVRP

•             MUX VLAN

•             sFlow

•             Hypertext Transfer Protocol Secure (HTTPS)

•             SSH1.5/SSH2

Podružné a pobočkové switche:

Požadovaný minimální počet portů pro jednotlivé lokace:

Zbraslav serverovna - 192 Ethernet 10/100/1000 ports, z toho min 20 ks PoE+ ports

Zbraslav přístavba, druhé a třetí patro - 48 Ethernet 10/100/1000 ports, PoE+

Zbraslav 1.patro - 24 Ethernet 10/100/1000 ports, PoE+

Brno - 48 Ethernet 10/100/1000 ports, PoE+

Pardubice - 24 Ethernet 10/100/1000 ports, PoE+

Specifikace:

•             24 x Ethernet 10/100/1,000 Base-T ports,4 10 Gig SFP+ port nebo 48 x Ethernet 10/100/1,000 Base-T ports, 4 x 10 Gigabit SFP+ ports (viz. požadované počty portů pro jednotlivé lokace)

•             Forwarding performance: 144 Mpps

•             Switching capacity: 336 Gbit/s

•             POE+

SECURITY

•             Hierarchical user management and password protection

•             DoS attack defense, ARP attack defense, and ICMP attack defense

•             Binding of the IP address, MAC address, interface number, and VLAN ID

•             Port isolation, port security, and sticky MAC

•             MFF

•             Blackhole MAC address entries

•             Limit on the number of learned MAC addresses

•             IEEE 802.1x authentication and limit on the number of users on an inte

•             rface

•             AAA authentication, RADIUS authentication, HWTACACS+ authentication, and NAC

•             SSH V2.0

•             Hypertext Transfer Protocol Secure (HTTPS)

•             CPU defense

•             Blacklist and whitelist

•             DHCP relay, DHCP server, DHCP snooping

•             DHCPv6 relay, DHCPv6 server, DHCPv6 snooping

MANAGEMENT

•             iStack

•             Virtual Cable Test (VCT)

•             Remote configuration and maintenance using Telnet

•             SNMPv1/v2c/v3

•             RMON

•             eSight and web-based NMS

•             HTTPS

•             LLDP/LLDP-MED

•             System logs and multi-level alarms

•             802.3az EEE

•             Dying Gasp